Фрагмент перевода технического текста с русского языка на английский

(тематика – вертолетовождение, радиоаппаратура)

| Оригинал | Перевод |
| --- | --- |
| Радиокомпас обеспечивает непрерывный отсчет курсового угла радиостанции (КУР) и позволяет: совершать полет на радиостанцию и от нее с визуальной индикацией курса; автоматически определять пеленг на радиостанцию по указателю курса с использованием магнитного компаса; работать как средневолновый радиоприемник в диапазоне частот 150 – 1300 кГц. Радиокомпас может использоваться в следующих режимах работы: Режим «Компас» является основным рабочим режимом радиокомпаса. В этом режиме радиокомпас при настройке его на частоту пеленгуемой радиостанции автоматически устанавливает стрелку индикатора курса в положение, соответствующее курсовому углу на эту радиостанцию. При этом сигналы радиостанции прослушиваются с помощью телефонов на выходе радиокомпаса. В режиме «Антенна» радиокомпас используется как обычный средневолновый связной приемник с достаточно высокой чувствительностью. В телефоны, включенные на выходе радиокомпаса, могут прослушиваться сигналы станций, работающих как модулированными, так и немодулированными колебаниями. | The radio compass provides continuous relative bearing measurement of the radio station and allows: to conduct a flight to and from the radio station visually indicating the direction; to find automatically direction to the radio station by the heading indicator using a magnetic compass; to operate as a medium-wave radio receiver in frequency band from 150 to 1300 kHz. The radio compass may be used in the following operating modes: «Compass» mode is the main operation mode of the radio compass. In this mode the radio compass takes bearings of the radio station to which it is tuned and automatically sets the pointer of the direction indicator coupled to position that corresponds to helicopter relative bearing to the radio station. The signals of usable radio station are audio identified by means of telephones connected to the radio compass output. In «Antenna» mode the radio compass is used as a regular medium-wave communication receiver with quite a high response. Through telephones connected to the radio compass output it is possible to listen to signals of stations operating both in modulating or non-modulating oscillations. |